## Slide 1: Wireless Transmission
Unguided Transmission Media

## Slide 2: Wireless Transmission
Three techniques:
  Microwave
      Terrestrial Microwave
      Satellite Microwave
  Broadcast Radio
  Infrared

## Slide 3: Wireless Transmission Frequencies
Three range of frequencies are considered here:
  1GHz(109 Hz )to 40GHz
    Referred as Microwave frequencies
    Highly directional beams are possible
    Suitable for Point to point transmission
    Satellite
  30MHz to 1GHz
    Microwave frequency
    Used for Omnidirectional applications
    Also referred as radio range
    Suitable for Broadcast radio
  3 x 1011 to 2 x 1014 Hz
    Infrared portion of the spectrum
    Local i.e for point-to-point and multi-point application within confined areas such as single room

## Slide 4: Wireless Transmission
For unguided media ,transmission and reception are achieved by means of an antenna

## Slide 5: Antennas
Antenna is an electrical conductor (or system of conductors) used to radiate electromagnetic energy or collect electromagnetic energy
Transmission
  energy from transmitter is converted to electromagnetic energy by the antenna
  Radiated into surrounding environment(atmosphere,space or water)
Reception
  Electromagnetic energy impinging on antenna is
  converted to radio frequency electrical energy
  Fed to receiver
For two way communication same antenna often used for both transmission and reception

## Slide 6: Antenna
Radiation Pattern:Power radiated in all directions
Not same performance in all directions
Common way to characterize the antenna is its radiation pattern
Isotropic antenna is (theoretical) point in space
  Idealized antenna
  Radiates in all directions equally
  Gives spherical radiation pattern with antenna at the center

## Slide 7: Parabolic Reflective Antenna
Used for terrestrial and satellite microwave transmission
Parabola is locus of point equidistant from a line and a point not on that line
  Fixed point is called focus
  Fixed line is called directrix
Revolve parabola about axis to get paraboloid
  Cross section parallel to axis gives parabola
  Cross section perpendicular to axis gives circle

## Slide 8: Parabolic Reflective Antenna

## Slide 9: Parabolic Reflective Antenna
  Such surfaces are used in microwave antennas due to the following property:
    If source of electromagnetic energy is placed at focus and if the paraboloid is a reflecting surface ,then waves get reflected from parabola in lines parallel to axis of paraboloid
    Creates (theoretical) parallel beam of light/sound/radio,but in reality there will be certain dispersion
    On reception,if incoming waves are parallel to the axis of reflecting paraboloid,the resulting signal will be concentrated at focus, where detector is placed

## Slide 10: Antenna Gain
Measure of directionality of antenna
Definition:
  Power output, in particular direction ,compared to that produced in any direction by isotropic antenna(omnidirectional)
Measured in decibels (dB)
Due to increased power radiated in a given direction thereby results in loss in power in another direction

## Slide 11: Antenna Gain and Effective Area
Relationship between antenna gain and effective area
    G = antenna gain
    Ae = effective area
    f = carrier frequency
    c = speed of light (» 3 ´ 108 m/s)
     = carrier wavelength

## Slide 12: Terrestrial Microwave
Physical Description
  Common microwave antenna is the “Parabolic dish”
  Size is about 3 m in diameter
  The antenna is fixed rigidly and focuses a narrow beam
  Line-of-sight transmission is achieved to the receiving antenna
  Antennas are located at substantial heights above ground level
  To extend the range between antennas and to be able to transmit over intervening obstacles
  To achieve long distance transmission ,a series of microwave relay towers is used and point-to-point links are strung together

## Slide 13: Terrestrial Microwave
Applications
  Primary use in long haul telecommunication service
  as an alternative to coaxial cable or optical fiber
  Used for voice and television transmission
  Used for short point-to-point links between buildings
  Used in cellular systems

## Slide 14: Terrestrial Microwave
Transmission characteristics
  Common frequencies used for transmission are in the range 1 to 40 GHz
  Higher the frequency ,the higher the potential bandwidth and therefore the higher the potential data rate
  The main source of loss is attenuation
  The loss is expressed as:
  L=10 log (4πd/λ)2 dB
  Where d is the distance and λis the wavelength ,in the same units
  i.e loss varies as a square of distance

## Slide 15: Terrestrial Microwave
  Therefore large repeater spacing is needed -10 to 100 km
  Attenuation increases with rainfall
  Another source of impairment is interference
  Transmission areas overlap and interference is always a danger
  Assignment of frequency bands is strictly regulated

## Slide 16: Satellite Microwave
A communication satellite is a relay station
Used to link two or more ground-based microwave transmitters/receivers,known as earth stations
Satellite receives on one frequency band(uplink), amplifies or repeats signal and transmits on another frequency band(downlink)
A single orbiting satellite will operate on a number of frequency bands ,called transponder channel or simply transponders
Two common configurations in satellite communication is as follows:

## Slide 17: Satellite Point to Point Link

## Slide 18: Satellite Broadcast Link

## Slide 19: Satellite Microwave
In the first ,the satellite is being used to provide a point-to-point link between two distant ground based antennas
In the second,the satellite provides communications between one ground based transmitter and a number of ground based receivers

## Slide 20: Satellite Microwave
To work effectively,satellite requires geo-stationary orbit
  Height of 35,784km
  i.e. the period of rotation of satellite will be equal to period of rotation of earth
  Otherwise it will not be at line of sight with the earth station at all times

## Slide 21: Satellite Microwave
Two satellites using the same frequency bands ,if close to each other ,will interfere with each other
To avoid this a 4o spacing (angular displacement as measured from earth) in the 4/6-GHz band and 3o spacing at 12/14 GHz

## Slide 22: Satellite Microwave
Applications
  Television
  Long distance telephone
  Private business networks

## Slide 23: Satellite Microwave
Transmission characteristics
  Frequency range in satellite communication is 1 to 10 GHz
  Below 1 GHz there is significant noise from natural sources
  Above 10 GHz the signal is severely attenuated by atmospheric absorption and precipitation

## Slide 24: Satellite Microwave
Disadvantages
  Because of the long distance involved ,there is a propagation delay(about a quarter second)
  Also introduces problems in error control and flow control
  Satellite is inherently broadcast facility

## Slide 25: Satellite Microwave
Types of frequency bands:
  4/6
    Uplink frequency:5.925 to 6.425
    Downlink frequency:3.7 to 4.2 GHz
  12/14
    Uplink frequency:14 to 14.5GHz
    Downlink frequency:11.7 to 12.2 GHz
  20/30
    Uplink frequency:27.5 to 30.0GHz
    Downlink frequency:17.7 to 20.2 GHz

## Slide 26: Broadcast Radio
Physical description
  Omnidirectional
  So it does not require dish shaped antenna
Applications
  FM radio
  UHF and VHF television
  Radio:Frequency range is 3kHz to 300GHz
  Broadcast radio:cover VHF and part of UHF band i.e. 30MHz to 1 GHz

## Slide 27: Broadcast Radio
Transmission characteristics
  The range 30MHz to 1 GHz is an effective one for broadcast communication
  The ionosphere is transparent to this frequency range
  Transmission is limited to the line- of- sight
  Distant transmitters will not interfere with each other due to reflection from the atmosphere
  Broadcast radio waves are less sensitive to attenuation from rainfall
  Because of the longer wavelength ,radiowaves suffer relatively less attenuation

## Slide 28: Broadcast Radio
Disadvantage
  Primary source of impairments in radio waves is multipath interference
  Reflection from land ,water and natural or human made objects can create multiple paths between antennas

## Slide 29: Infrared
Infrared communicatins achieved using transmitters /receivers(transceiver) that modulate noncoherent infrared light
Transcievers must be within Line-of-sight of each other directly or via reflection from light-coloured surface such as ceiling of a room
Blocked by walls(while microwave penetrate through walls)
e.g. TV remote control

## Slide 30: Wireless Propagation
A Signal radiated from an antenna travels along one of three routes
  Ground wave
  Sky wave
  Line- of -sight
    Above 30Mhz
    May be further than optical line of sight due to refraction
    More later…

## Slide 31: Ground Wave Propagation
  Ground wave
    Signal follows contour of earth i.e the curvature of the earth
    Effect can be found in frequencies up to 2MHz
    AM radio

## Slide 32: Ground Wave Propagation

## Slide 33: Sky Wave Propagation
  Sky wave
    Amateur radio, BBC world service, Voice of America
    Signal from an earth based antenna is reflected from ionosphere layer of upper atmosphere(ionosphere) back to the earth
    Actually it is refraction
    Signal an travel through a number of hops ,bouncing back between ionosphere and earth’s surface
    With this propagation mode ,a signal can be picked up thousands of kilometers from the transmitter.

## Slide 34: Sky Wave Propagation

## Slide 35: Line- of -sight
  Line- of -sight
    Above 30MHz
    May be further than optical line of sight due to refraction
    For satellite communication as well as ground based communication ,transmitter and receiver must be within effective line of sight of each other

## Slide 36: Line of Sight Propagation

## Slide 37: Refraction
Velocity of electromagnetic wave is a function of density of material
  ~3 x 108 m/s in vacuum, less in anything else
As wave moves from one medium to another, its speed changes
  Causes bending of direction of wave at boundary
  Towards more dense medium
Index of refraction (refractive index) is
  Sin(angle of incidence)/sin(angle of refraction)
  Varies with wavelength
May cause sudden change of direction at transition between media
May cause gradual bending if medium density is varying
  Density of atmosphere decreases with height
  Results in bending towards earth of radio waves

## Slide 38: Optical and Radio Horizons

## Slide 39: Line of Sight Transmission
Free space loss
  Signal disperses with distance
  Greater for lower frequencies (longer wavelengths)
Atmospheric Absorption
  Water vapour and oxygen absorb radio signals
  Water greatest at 22GHz, less below 15GHz
  Oxygen greater at 60GHz, less below 30GHz
  Rain and fog scatter radio waves
Multipath
  Better to get line of sight if possible
  Signal can be reflected causing multiple copies to be received
  May be no direct signal at all
  May reinforce or cancel direct signal
Refraction
  May result in partial or total loss of signal at receiver

## Slide 40: Free Space Loss

## Slide 41: Multipath Interference